## Slide 1: EKF-SLAM Monte Carlo Localization
Reza Ghabcheloo
IHA 4306 Moro

## Slide 2: Content
Data association
Simultaneous Localization and Mapping (SLAM); focus EKF-SLAM
Monte Carlo Localization (MCL)
Ref:
Principles of Robot Motion: Theory, Algorithms, and Implementation
by Howie Choset et al.
Intro to Autonomous Mobile Robots, R. Siegwart et al

## Slide 3: Question, localization
Q. We have an omni-directional robot moving on a line on a plane. Odomtery uncertainties are the same in all the x, y, heading. If we measure distance to a wall, plot the localization uncertainty progress.

## Slide 4: Map
A topological representation 
Significant places of the environment (discrete state space)
Metric representation:
Fine grid (10-30cm, 2-10deg)
Features (continuous state space)

## Slide 5
Examples from Siegwart

## Slide 6: Feature / landmark
Raw sensor data
Feature extraction
Uncertainty models

## Slide 7: SLAM

## Slide 8: Data association

## Slide 9: Data Association
Localization: In practice, landmarks have similar properties which make them good features but often make them difficult to distinguish one from another. When this happens, we must address the problem of data association, which is the question of which landmark corresponds to a particular measurement. Mahalanobis norm: the fittest landmark
SLAM: We must determine which landmark corresponds to each measurement. We also have to determine when a new landmark has been encountered. Adding features to the map as they arrive / become visible

## Slide 10: Data association, algorithm
Find the most fit feature from the map
Use the feature for localization
EKF review…

## Slide 11: EKF: nonlinear filter 1/3
,
Prediction
Expected measurement
With known landmarks

## Slide 12: EKF: nonlinear filter 2/3
Covariance of state estimation error, a prior
Kalman gain
Posterior
Covariance of innovation

## Slide 13: Find the most fit feature from the map
Innovation with known correspondence (time index is dropped)
Landmark ; Measurement
The difference between actual measurement and the measurement we would expect if correspond to th landmark

## Slide 14: Example
=

## Slide 15: Data association
The smaller the error , the more likely it is that the measurement corresponds to landmark
however, not all the measurements are equally certain…

## Slide 16: Using Mahalanobis distance
The notion of small weighted or normalized by prediction uncertainty, that is, Mahalanobis distance
Then find the that minimizes

## Slide 17: Mahalanobis distance
Mahalanobis distance indicates how far away the point is from the mean in units of standard deviation
)=
where is the covariance matrix
Matlab
mvnrnd(.)
mahal(.)
Note: =0.4545

## Slide 18: Data association, summary
Find the most fit feature from the map, by finding the that minimizes , call it
Use feature for localization

## Slide 19: EKF SLAM

## Slide 20: SLAM
Build a map and localize yourself in that map concurrently
In this lecture:
  online EKF SLAM

## Slide 21: Maps for planning and obstacle avoidance
Landmark maps not useful for planning
A common approach is two stage solution: Perform
  SLAM to build a landmark map; then
  Occupancy grid map with know pose

## Slide 22: Maps for planning and obstacle avoidance
  One common solution is to build a feature map (SLAM) and then knowing the pose build an “occupancy grid map with know pose”
Feature map
Occupancy grid map

## Slide 23: EKF, review
Uncertainties are unimodal: ellipsoids

## Slide 24: EKF SLAM
Blue dots are landmarks (initially unknown)
Dash line: robot path
Gray: robot pose belief
Red: landmarks position belief
Uncertainty of all the landmarks and the robot pose is reduced, as soon as the first landmark is revisited!

## Slide 25: EKF SLAM
Left column: the robot and the landmarks
Right column : covariance matrix
After a while all the landmark locations become correlated

## Slide 26: EKF SLAM
State vector includes: robot pose and landmark positions
Motion model:
Robot motion models and range and bearing measurements the same as in localization

## Slide 27: EKF: nonlinear filter 1/3
,
Prediction
The state vector is now much larger!
So are , , , and

## Slide 28: EKF: nonlinear filter 2/3
Covariance of state estimation error, a prior
Kalman gain
Posterior

## Slide 29: EKF SLAM
Q: If there are 3 landmarks in the map so far, what are the sizes of the state vector and the other matrices of the algorithm , , , and ?
Q: Let’s calculate one row of as an example

## Slide 30: EKF SLAM Algorithm
Initialize the SLAM vector with the robot pose the center of the map! That is arbitrary
Augment the landmark position to the vector as soon as it is seen, and construct the corresponding matrices and augment/modify , , , , ,

## Slide 31: Adding new landmark to the map, when the landmarks are not distinguishable
Calculate the innovation for each combination of landmarks (already in the map) and measurements
Check the minimum against an acceptance threshold
If the minimum is above a high threshold, initialize and add the landmark to the map.

## Slide 32: Monte Carlo localization
Bayes filter review…

## Slide 33: Bayes filter
Sequentially solved in two steps:
Prediction
Update
MCL
Notice the difference,
we will come back to this

## Slide 34: Distributions representation of belief
Discrete space: Histogram filter
Particles: MC (Monte Carlo) filter
Parametric: (Extended Kalman Filter) EKF

## Slide 35: Monte Carlo localization
Based on Monte Carlo sampling
Also called Particle filter localization
Survival of the fittest
Can represent non Gaussian distributions

## Slide 36: Monte Carlo Localization (MCL), notation
N: Number of samples
Motion model
: probability of measuring , if the robot was at particles
the time index
set of samples (particles) and their importance

## Slide 37: Particles representing distributions
In MCL, posterior is represented by a set M of pairs samples (particles) and their importance weight
Gaussian is mapped using function g(.) --> Not Gaussian anymore

## Slide 38: Function approximation
Samples from a uniform distribution and importance weight proportional to the probability
More samples drawn from intervals with higher probabilities
A
B

## Slide 39: Resampling
Resampling is the problem of: given the set of samples (A) with importance
weight , how to generate samples (B) equally important
, representing the original function. In other words, probability of
the sample is proportional to its weight: survival of the fittest
Resampling is expensive, so resample only when the number of effective
number of samples under a threshold (say N/10)
Q: Can you come up with an algorithm to do resampling, given we know
how to draw samples from uniform distribution?
Matlab: xi= datasample(xi,…,'weights', wi’s)

## Slide 40: MCL, algorithm at time k also called bootstrap filter
For i=1:N
Sample from
Compute importance weight
Add the particle to the set
Endfor
For i=1:N
Normalize weights
Endfor
Resample if needed: after resampling ; weights remain unchanged if no resampling done
Return M(k): mean(
Three main parts
Sample from motion model
Calculate the importance weight
Resample

## Slide 41: MCL
Map ={1,…,6}
Resampling:
Ensures that the particles survive only in meaningful parts of the state space (where the weights are not negligible)

## Slide 42
MCL capable of global localization
in contract to EKF
It also does pose tracking

## Slide 43: Importance weights
It is easy if observation model and uncertainties are
=
Q: What if there are two independent measurements?
Matlab: normpdf(z, mean, cov)
Three main parts
Sample from motion model
Calculate the importance weight
Resample

## Slide 44: Sampling motion model 1/2
Samples can be drawn from Normal distribution and use
Matlab: randn(), mvnrnd()
Q: What us difference if and are independent or dependent?
and then calculate a sample predication

## Slide 45: Sampling motion model 2/2
robotics.OdometryMotionModel class; Gaussian noise 4-element vector
Rotational error due to rotational motion
Rotational error due to translational motion
Translational error due to translation motion
Translational error due to rotational motion

## Slide 46: Conditioning on the obstacle map
How to tell the filter that is impossible that the robot is inside a wall?
  First sample motion model without map
  Accept only samples that lie in free space
This improves sampling but ignores the case that some sample may pass through the obstacles, if odometry translations are large

## Slide 47: Mont Carlo Localization
http://robots.stanford.edu/movies/sca80a0.avi using Laser range finder
http://robots.stanford.edu/movies/Sampling2.avi Ceiling maps

## Slide 48
Tutorial on Simultaneous Localization and Mapping: Part I and II, 2006
HUGH DURRANT-WHYTE AND TIM BAILEY

## Slide 49: Other topics
Adding random samples to account for probability of unmolded behaviors/scenarios
Detection of failure: average observation likelihood , if threshold, reinitialize global localization
Issues: stationary robot
FastSLAM, Rao-Blackwellized filter

## Slide 50: FastSLAM, Rao-Blackwellized filter
Essence:
  motion model represented by Monte Carlo sampling and
  Observation (bearing, range) is linearized
benefiting from both EKF and MCL

## Slide 51: Mapping with known pose
Given a point observation (reflection from the environment), how to build a probabilistic map: a grid map, which each of its cell are probability of being occupied.
See Matlab function:
insertRay (.) from
Class: robotics.OccupancyGrid
Model of one ray