## Slide 1: Lecture 6: Path planning and uncertainties
Risto Ritala
Sept 24, 2018
IHA-4306 Fundamentals of mobile robotics

## Slide 2: Sources of uncertainty
Consequences of actions are not known completely
  Probabilistic model
  No model at all
Costs of actions are not known completely
Sensing capabilities are not complete
  Current system state is not known (localization problem)
Map of environment is not known completely
Communication in multi-robot system is not completely reliable
  Robots cannot communicate their current states and thus the global state is not known completely
In this course
  Consequences of actions (this lecture)
  Single robot state & incomplete sensing
  Mapping
  Intro to simultaneous localization and mapping (SLAM) and decision making under all these uncertainties (POMDP)

## Slide 3: Sources and consequences of uncertainty
?

## Slide 4: Uncertain actions, known state
Consider making an action a (such as choosing an edge) at node n. Assume that we do not know
exactly to which node the action is taking us but we know:
Probability of ending at n2 as a result of action a at n1.
Cost when taking the action a at n1 and resulting in n2.
Dynamic programming generalizes straight forwardly to this case:
Solving this by iteration works as in the deterministic case. Dijkstra or A* do not generalize to uncertain actions.

## Slide 5: A simple example
Action is choosing an edge. Result is succesful transition
or staying in the start node; success rate is denoted p, cost
depends only on the action:
Blue arrows: p = 0.9, c = 1
Green arrows: p = 0.3, c = 0.3
Red arrows: p = 0.95, c = 2.5
Purple node is the goal where one can only stay.
Find the optimal action at all sites.
1
7
6
5
4
3
2
4.4
1.1
2.6
2.2
3.6
3.3
4.7
optimal

## Slide 6: Model-free planning: Q-learning
http://mnemstudio.org/path-finding-q-learning-tutorial.htm
What if we do not know
or but can only try actions and see what happens.
First DEFINE:
Suppose we are at state n, make an action a and find ourselves as a result of this at some state n’. We have
Observed the corresponding reward and generated a sample of transitions and can make an update as
where the right hand side is based on our earlier estimates of Q and 0 < g < 1 is the ”learning rate”. This can be
shown to converge when learning rate is reduced to zero as time goes infinite.

## Slide 7: Model-free planning: Q-learning
Questions about practical implementations:
  How to initialize Qs?
    One approach: set them zero.
  How to choose g?
    Most commonly chosen as a constant, such as 0.1
  How to choose actions to obtain a good decision making?
    Balance between
      exploration = seek for new opportunities
      exploitation = choose an action that is deemed the best based on current Q
  How to deal with large systems?
    Q(n,a;ng) can be approximated with e.g. neural networks or other function approximators to deal with even continuous valued states.

## Slide 8: A simple example
1
7
6
5
4
3
2
4.3
1.2
2.5
2.5
3.5
3.4
4.6
With Q-learning
Initialize all Q=0
Set g = 0.2
At node n set the probabilities of the actions to be
b=1; and select action according to these probabilites
(small b: actions are almost equally likely; large b: the action
Currently considered the optimal is strongly favored)
Simulate with starting point randomly any 1..7; when hits
the state 8, start again; 500 restarts
Finds the policy which is the same as with model-based
case (but of course requires much more computation).
J-values differ only by 0.1.

## Slide 9: Main points
We dealt with system uncertainties, but assumed that at all times, the state of the system is known
If results of actions are not deterministic and there is a probabilistic model
  Dynamic programming generalizes straight forwardly
  Dijkstra and A* do not generalize to uncertain actions
If there is no model
  Q-learning works, but requires a simulator or a large number of real-world experiments
NEXT: incomplete information about the state