## Slide 1: Practical session with ABB robots
ASE-9407 Robot Manipulators: Modeling, Control and Programming

## Slide 2: Outline
FASTory introduction
Core concepts
Assignment 2 kickoff
Tips
Targets teaching

## Slide 3: Core concepts
Main Components
Joints and links
Degree of Freedom (DOF)
Orientation
Tool, Tool Central Point (TCP)
Coordinate system
Cartesian and joint movement
Inverse kinematics, Reachability, Singularities
Robot configurations

## Slide 4: Main Components
Controller
Drives
Manipulator
Teach pendant
PC-RS
Tool

## Slide 5: IRB 140
Multipurpose
6 kg payload
Reachability 810 mm
Axis 1 rotation 360 degrees
Main applications
  Arc welding
  Assembly
  Cleaning/Spraying
  Machine tending
  Material handling
  Packing
  Deburring

## Slide 6: Joints and links

## Slide 7: Degrees of Freedom (DoF)
Position and orientation
3 DoF
[x,y,z]
4 DoF
[x,y,z,θ]

## Slide 8: Degrees of Freedom (DoF)
6 DoF
DoF related with the number of joints (degree of mobility)

## Slide 9: Orientation
Euler angles
Quaternions
Gimbal Lock

## Slide 10: Tool Central Point (TCP)

## Slide 11: Tool Central Point (TCP)

## Slide 12: Tool Central Point (TCP)

## Slide 13: Tool Central Point (TCP)

## Slide 14: Coordinate system (reference frame)
{C1}
{C2}
target

## Slide 15: Other concepts
Linear (Cartesian) and joint movement
Inverse kinematics:
  compute the joints to achieve position+orientation
Reachability
Singularities

## Slide 16: Robot configuration

## Slide 17: Robot Studio
RobotWare
System layout
Offline programming
Emulate physical components:
  Teach pendant
  Robot controllers
RAPID editor

## Slide 18
Robot Studio: tool
Rapid: programming language
RobotWare: Firmware inside the robot controller
RobotWare: 5.15.14

## Slide 19: Robot Studio: Pick and place flow
Design 3D system
Define work objects / targets
Synchronize controller
Create flow control on RAPID code
Set/fix orientations
Offline testing
Deploy
Fix targets positions by teaching/updating targets

## Slide 21: Robot Studio: Path creation flow
Design 3D system
Define work objects / targets
Create path
Synchronize controller
Set/fix orientations
Modify/create RAPID code
Test
Deploy

## Slide 22: Assignment 2 Kickoff

## Slide 23: Teaching targets with the teach pendant

## Slide 24: Robot studio
RSPAG files
Network license
Robotware 5.15.14 for Task 2